## Slide 1: SNNs for Fast-Moving Object Detection

## Slide 2: Ball Throws
Simulated
  Plan A: With Isaac Sim (Maybe not worth it)
  Plan B: Just with Python
Real
  To check the output of the event camera

## Slide 3: Video to events
V2E -> Colab
VID2E
V2CE
ESIM
Plenty of options. Whichever that looks like the real event camera output.

## Slide 4: Literature review
Event-Based Trajectory Prediction Using SNNs
  Event camera with spatial filtering
  SCNN with STDP (unsupervised)
  They predict the height of the ball and the x for two possible x values (left or right) in a 2d parabola
  RMSE
  We don’t need unsupervised training (as long as the simulator is good enough). Maybe better results.
  Preprocessing the data will increase the inference time
  We would predict the impact point on a fixed plane.

## Slide 5: Literature review
Detection of Fast-Moving Objects with Neuromorphic Hardware
  SCNN
  With ROI defined on the last known ball position.
  Diff. Architectures and training method depending on the spiking chip used.
  Classification problem to find the pixel for the ball position (2d)

## Slide 6: Literature review
SCTN: Event-based object tracking with energy-efficient deep convolutional spiking neural networks
  3 layer SCNN + 3 FCL
  Learning algorithm STCA (supervised)
  They sample 256 possible boxes around the expected target positions and they check the one with more spikes. Seems like a very suboptimal and slow approach.

## Slide 7: Literature review
Robotic goalie with 3 ms reaction time at 4% CPU load using event-based dynamic vision sensor
  Cluster tracker algorithm (no SNN)
  Goalie calibration
  Explanation of USB interfaces for sensors and actuators (maybe relevant in the future)

## Slide 8: Literature review
Event-based Agile Object Catching with a Quadrupedal Robot
  Two phases: trajectory estimation + robot actuation
  Trajectory estimation
    Moving object detection DBSCAN clustering algorithm
    Remove outliers with RANSAC then fit to a parabola
    Find intersection with the plane
    No SNN

## Slide 9: Literature review
Event-Based Angular Velocity Regression with Spiking Networks
  Regression problem (continuous values of angular velocity)
  Global Average Spiking Pooling to avoid last FCL
    Less parameters
    Improved robustness to spatial translation
  Results could be better, but they didn’t learn the hyperparameters (potential improvement)
  Code available uzh-rpg/snn_angular_velocity: Event-Based Angular Velocity Regression with Spiking Networks

## Slide 10: Literature review
TossingBot: Learning to Throw Arbitrary Objects with Residual Physics
  Residual physics: DL to learn a residual on top of the physics result
  Apart from that the problem is very different. No object tracking nor trajectory estimation.

## Slide 11: Approach
Events -> Trajectory (regression problem. Complex and slow)
Events -> Impact point (assuming no additional movement of the robot)
  Classification task
  Problems: many trajectories don’t have impact point.
  Solutions:
    Training two models, one for checking if there is an impact point and one for finding it.
    Selecting carefully the training data.

## Slide 12: Plan A: Classification
ROI / Spatial filtering?
SCNN w/ surrogate gradient (easy to implement, supervised)
GASP
Classification on X and Y in the goal

## Slide 13: Plan B: Regression
ROI / Spatial filtering?
SCNN w/ surrogate gradient
GASP
Position and velocity of the ball
I would say this is too difficult

## Slide 14: SNN Architecture
Options
  RSNN
    LSM
      Few hyperparameters
      Fast inference and fast training
    SLSTM
      More hyperparameters
      Best results
      Slow training
    SGRU
      Fast inference and fast training

## Slide 15: SNN Architecture
Non recurrent
  SCNN + LIF
  SCNN + Transformer
Hybrid
  SCNN + RSNN

## Slide 16: Approach
SCNN + LIF (Should be enough as the velocity is encoded in each frame)
If it is not accurate enough -> SCNN + SGRU / SCNN + LSM
If it is still not accurate enough -> SCNN + SLSTM
- inference time +

## Slide 17: Plan C: RNN
SCNN + LSM
Is a good way of adding temporal processing (in case the SCNN fails on that)
Limited literature on the topic.

## Slide 19
All that use SNNs do it in 2d. Maybe add another camera and do it in 2d?
Binary classification goal/not goal. Then find the impact point.
Take into account robot position.
ROI with changing size. This is possible because neurons with no input have no spikes thus no computation is done.