## Slide 1: SPIKING NEURAL NETWORKS FOR FAST-MOVING OBJECT DETECTION
Mario Real Enrique

## Slide 2: Problem Statement
Conventional cameras either introduce huge latencies or generate too much data
Problem for real-time ball trajectory prediction
We want to leverage event cameras and SNNs to extract the relevant information for the vision system of the goalkeeper (RoboCup).
2 pieces:
  Data
  Model

## Slide 3: Data
Real event data of ball throws
  Positive and negative events
Labeled using OpenCV
Data and labels get reduced by a factor of 2 for reduced training times

## Slide 4: Initial Approach
Ball detector on images
  Input: Positive and negative events (2 channels) accumulated during 10ms
  Output: X,Y pixel prediction of the ball on the image.
Motivation
  Easier problem
  Initial estimation of accuracy, training times and latency
EVENT DATA
2 channels
(+, -)
3 Layer SCNN
X SFCL
Y SFCL
X prediction
Y prediction
Argmax()
Argmax()

## Slide 5: Training
Images were shuffled
Each image was shown to the SNN for 20 time steps
Trained for 50 epochs
Results
  Training time: 3h 40 min
  Inference time: 40ms
  Avg error: 5,13 px
  95% CI error: 13,36 px
Original image 680x408

## Slide 6: Next steps:
Simulated data with IsaacSIM
  Better labels
  More diverse data
  Problems encountered:
  “Shadow” when moving the ball
  Difficulty setting up the camera parameters

## Slide 7: Next steps
Video to event data
  Implement locally
  ESim, Vid2E, V2E
Approaches
  Dual camera ball tracker
  Ball tracker + radius estimation
  Goal hit point predictor
Decreasing inference time

## Slide 8: Uncertainty estimation: naive approach
Worst case scenario
  Ball moving at 10 m/s at 10 m from the camera
  95 percentile worst pixel error (13,36 px)
  Time interval between collections of events: 1ms
Two components
  1 pixel in the real world * error in pixels
  Velocity * time interval

## Slide 9: Uncertainty estimation: formal approach
The idea is to propagate the 3D position uncertainty in time for trajectory estimation
The resulting position uncertainty should be less than half the size of the robot
This would serve as a higher bound for the error in the classification task
A Kalman Filter would be needed for calculating the uncertainty of the velocity

## Slide 10: Questions
What is the expected uncertainty for the position of the robot and its orientation?
What do you think about the formal approach for uncertainty estimation?
Do the proposed approaches satisfy the needs of the team?